## Slide 1
1
Parameter | Min. |  | Typ. | Max. | Units
Frequency Range | 2.57-2.62 |  |  |  | GHz
Insertion Loss |  |  |  | 0.3 | dB
Isolation | 18 |  |  |  | dB
Average Power |  | 20 |  |  | W
PIMD 3rd |  | -65 |  |  | dBc
Return Loss | 18 |  |  |  | dB
Impedance |  |  | 50 |  | Ω
Connector | SMA-male/SMA-Female |  |  |  | 
Material | BODY: Steel/TAB: BeCu |  |  |  | 
Direction | CCW |  |  |  | 
Weight | - |  |  |  | 
Package Sealing | BODY: Nickel plate/TAB: Silver Plated |  |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+105℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The circulator is a coaxial circulator with a typical Loss insertion of 0.3 dB and a typical isolation of 18dB across the frequency range of 2.57 to 2.62 GHz. The circulator can handing average power of 20W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.