## Slide 1
1
Parameter |  | Min. | Typ. | Max. | Units
Frequency Range |  | 0.99-1.13 |  |  | GHz
Insertion Loss |  |  |  | 0.5 | dB
Isolation | @Δ&Σ | 25 |  |  | dB
 | @L&R | 15 |  |  | dB
VSWR | @Δ&Σ |  |  | 1.3 | -
 | @L&R |  |  | 1.25 | -
Amplitude Unbalance | L&R@Δ/Σ |  |  | ±0.25 | dB
Phase Unbalance | L&R@Δ |  |  | 180±2 | °
 | L&R@Σ |  |  | ±2 | °
Power Handling |  |  | 20 |  | W
Impedance |  |  | 50 |  | Ω
Connector |  | 0.38 Microstrip Needle |  |  | 
Material |  | Aluminum |  |  | 
Weight |  | /g |  |  | 
Package Sealing |  | Silver plated (Standard) |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+125℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The Hybrid is a broadband 180° Hybrid with The Nominal Coupling nominal is 3 dB and a high isolation of 25dB across the frequency range of 0.99 to 1.13 GHz. The power divider can reach handling power 20W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.