## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 26.5-40 |  |  | GHz
Insertion Loss |  | 1.6 | 1.7 | dB
Isolation | 12 | 14 |  | dB
VSWR |  | 1.6 | 1.8 | -
Forward Power (CW) |  |  | 10 | W
Reverse Power (CW) |  |  | 1 | W
Impedance |  | 50 |  | Ω
Input Connector | 2.92-Female |  |  | 
Output Connector | 2.92-Male |  |  | 
Material | Aluminum |  |  | 
Weight | 35g |  |  | 
Package Sealing | Nickel Plated |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+105℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The Isolator is a coaxial isolator with a typical insertion loss of 1.6 dB and a typical isolation of 14dB across the frequency range of 26.5 to 40 GHz. The isolator can reach handling average power of 10W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.