## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 2-4 |  |  | GHz
Insertion Loss |  |  | 0.65 | dB
Isolation | 17 |  |  | dB
VSWR |  |  | 1.35 | -
Forward Power (CW) |  | 60 | 100 | W
Rotation | Clockwise (Standard) Counter Clockwise (upon request) |  |  | 
Impedance |  | 50 |  | Ω
Connector | SMA-Female |  |  | 
Material | Aluminum |  |  | 
Weight | /g |  |  | 
Package Sealing | Nickel Plated |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+105℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The circulator is a coaxial circulator with a typical insertion loss of 0.65 dB and a typical isolation of 17dB across the frequency range of 2 to 4 GHz. The circulator can reach handling average power of -W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.