## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 40-50 |  |  | GHz
Insertion Loss(Port 1 to Port 2 & Port 2 to Port 3) |  | 1.0 |  | dB
Isolation(Port 2 to Port 1 & Port 3 to Port 2) | 20 | 25 |  | dB
Insertion Loss(Port 3 to Port 1) |  | 30 |  | dB
Isolation(Port 1 to Port 3) | 16 | 18 |  | dB
Return Loss |  | 15 |  | dB
Forward Power (CW) |  | 10 |  | W
Reverse Power (CW) |  | 1 |  | W
Impedance |  | - |  | Ω
RF Input and Output | WR-22 Waveguide with UG-383/U Anti-Cocking Flange |  |  | 
Material | Aluminum |  |  | 
Weight | -g |  |  | 
Package Sealing | Gold Chem Film and Black Anodized |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+105℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The circulator is a coaxial circulator with a typical insertion loss of 1.0 dB and a typical isolation of 25dB across the frequency range of 40 to 50GHz. The circulator can reach handling average power of -W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.