## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 110-170 |  |  | GHz
Insertion Loss (excluding coupling) |  | 2.5 |  | dB
Normal Coupling |  | 20 |  | dB
Directivity | 20 | 25 |  | dB
Main Line Return Loss | 20 |  |  | dB
Power Handling |  | 20 |  | W
Impedance |  | / |  | Ω
Connector | WR-06 Waveguides with UG-387/U Anti-Cocking Flange |  |  | 
Material | Brass |  |  | 
Weight | /g |  |  | 
Package Sealing | Gold Plated (Standard) |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -40℃~+85℃
※ Storage Temperature | -45℃~+105℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The coupler is a single directional coupler with a typical Loss insertion of 2.5 dB and a typical directivity of 30dB across the frequency range of 110 to 170GHz. The directional coupler can reach handling power 20W. Accept customization according to different needs.