## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 0.3-0.5 |  |  | GHz
Insertion Loss |  | 0.4 | 0.6 | dB
Isolation | 20 | 22 |  | dB
VSWR |  | 1.3 | 1.4 | -
Amplitude Unbalance |  | ±0.3 | ±0.5 | dB
Phase Unbalance |  | ±5 | ±10 | °
Power Handling |  | 50 |  | W
Impedance |  | 50 |  | Ω
Connector | SMA-Female |  |  | 
Material | Aluminum |  |  | 
Weight | /g |  |  | 
Package Sealing | Gray Color(Standard) |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -45℃~+85℃
※ Storage Temperature | -55℃~+125℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The hybrid is a broadband 180° hybird with a typical insertion loss of 0.4 dB and a typical isolation of 22dB across the frequency range of 0.3 to 0.5 GHz. The directional coupler can reach handling power 50W. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.