## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 0.4-1 |  |  | GHz
Gain | 40 | 46 |  | dB
Gain Flatness |  |  | ±2.0 | dB
Input VSWR |  |  | 2.0 | -
Output VSWR |  |  | 2.0 | -
Output Power for (P1dB) | 40 |  |  | dBm
Spurious |  | -60 |  | dBc
Input Max Power(no damage) |  |  | 10 | dBm
DC Current (Vcc=+28V)(@Pout=10W) |  | 3 |  | A
Impedance | 50 |  |  | Ω
Input/Output Connector | SMA-Female/SMA-Female |  |  | 
DC Interface Connector | D-Sub 9-Pin, Male |  |  | 
Weight | - |  |  | 
Package Sealing | External Heatsink (Not included) |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | -25℃~+85℃
※ Storage Temperature | -55℃~+125℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The power amplifier is a 10W power amplifier with a typical small signal gain of 46 dB across the frequency range of 0.4 to 1 GHz. The typical output power P-1 40dBm. The DC power requirement for the amplifier is +12 VDC/3 A. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
***Heat Sink required during operation***
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.