## Slide 1
1
Parameter | Min. | Typ. | Max. | Units
Frequency Range | 81-86 |  |  | GHz
Gain |  | 30 |  | dB
Output Power for (P1dB) |  | 27 |  | dBm
Output Power for (PSAT) |  | 28 |  | dBm
Input Power |  |  | 5 | dBm
Input Return Loss |  | 10 |  | dB
Output Return Loss |  | 10 |  | dB
DC Voltage | 6 | 8 | 15 | VDC
DC Current (Vcc=+8V) |  | 1.8 |  | A
Input/Output Port | WR-12 Waveguide with UG-387/U Anticocking Flange |  |  | 
Material | Aluminium/Gold Painting |  |  | 
Weight | 1.6Oz |  |  | 
Package Sealing | General Sealing (Standard) |  |  | 
Electrical Specifications（+25℃）:
Radar Systems
Communication Systems
Receivers Systems
Environmental Specifications:
※ Operational Temperature | 0℃~+50℃
※ Storage Temperature | -25℃~+85℃
OBSERVE PRECAUTIONS ELECTROSTATIC SENSITIVE DEVICES
Description:
The amplifier is a power amplifier with a typ small signal gain of 30 dB across the frequency range of 81 to 86 GHz. The typ output power P-1 27 dBm. The DC power requirement for the amplifier is +8 VDC/1.8A. Accept customization according to different needs.

## Slide 2
Outline Drawing
All Dimensions in mm（inches） Tolerance ±0.25（0.01）
2
***Heat Sink required during operation***
NOTE:
1. The product is designed to meet environmental ratings but not tested. If you need to test environmental condition, please contact our sales department.
2. Miczen technologies co., Ltd. reserves the right to change the above information without notice.